## Slide 1: Hazard Hardware - Data Hazards
Read after write hazards (RAW)
The register file s8 here, cannot be updated in time for instructions sub and or to read
2nd instruction: sub s2, s8, s3
sub in E stage needs data that was just computed by the add, now in M stage
So we will add a ForwardAE and ForwardBE to forward data from M to E to the ALU input source here
3rd instruction: or s9, t6, s8
or in E stage needs data from add, now in W stage
So we will add a ForwardAE and ForwardBE to forward data from W to E as well here
4th instruction: and s7, s8, t2
and in D stage needs the register which is written to by the add only at the end of cycle, but the register is read at the same time, which will be the wrong data
So we also need W to D forwarding here
The register file AND the pipeline register E is then written at the same time

## Slide 2: Hazard Hardware - Data Hazards
3. Load and use hazard
lw s3, (s2)
xor s10, s3, s6
The register file s7 here, cannot be updated in time for instructions after lw
The subsequent instructions will need the register data in the E stage to compute the result. However, the data is only available when lw is in the W stage (after it has read from memory in the M stage)
So we stall one cycle (when and is in D stage -> E stage) to make lw W stage and the and E stage. Then the forwarding will be done from W to E (done previously)
2. Mem to mem copy
lw s3, (s2)
sw s3, (s1)
These two together, copies the data in address s2 to address s1
The register file here, s3, cannot be updated in time for sw to read in D stage.
sw in M stage needs the value of s3 to store into memory, which is provided only at lw in W stage (lw just finished reading from memory at its own M stage)
So we forward the data from W to M

## Slide 3: Hazard Hardware - HazardUnit
4. Control hazards
When we do a branch, the result of the branch and therefore the next PC is only computed at E stage
Therefore the correct instruction’s F stage will need the correct PC that the branch, now in M stage, provides. So we forward data from M to E (done previously)
More importantly, we need to flush the next two instructions if the branch is taken (when PCSrcE = 1). The instruction in decode (FlushE) and fetch (FlushD) will be flushed.
Note: To stall the instructions in F and D in load and use hazard, we will also need to FlushE so that the instruction in D (the use instruction) does not continue on to mess up other stuff (e.g. writing to memory, etc.)

## Slide 4: 2-bit Branch Predictor - Predictor Unit
Key details:
Tables to store both predicted outcome and predicted BTA
  Tables have 5-bit index each in our CPU → 32 entries and smaller margin of error (confusing other instructions with branch instructions / confusing 1 branch instruction for another branch instruction etc.)
2-bit predictor that starts at “weakly not taken” stage (01)

## Slide 5: 2-bit Branch Predictor - How it is Used
Key details:
PC_IN first checks if instruction is a jump instruction (either jal or jalr), and routes the next PC value to be the respective addresses
If not, it then checks if the branch was predicted correctly or not – if it is, use PCE + 4, if not, use PredictedPC.
PredictedPC checks whether the branch at F stage is predicted to be taken or not – if it is, look up the BTB for the predicted BTA, if not use PCF + 4.

## Slide 6: 2-bit Branch Predictor - Impact on Hazards
Key details:
Flushing should always happen for jump instructions (either jal or jalr), as well as if the branch was mispredicted.
Hence, FlushE and FlushD was modified to flush whenever any of the above happens as well.